## Slide 1: ECE 874 Course Organization
Instructors:
  Timothy Burg, tburg@clemson.edu
Book: Marquez – Nonlinear Control Systems – Analysis and Design
  You need access to the book. We will follow the organization of the book fairly closely.
Additional class notes will be provided.
All notes and solutions will be distributed using the class website and grades will be communicated using Blackboard. The website is located at http://www.eqpoint.info/nonlinearcourse
You may need to install a trail version of MathType to view the fonts in the slides (the fonts remain on the system even after the trial expires). See: http://www.dessci.com/en/support/mathtype/tsn/tsn50.htm
Office Hours: MWF 8-10 and as needed (email for appointment). 1058-C Rathbone Hall

## Slide 2: ECE 874 Course Organization
Homework at 5% and four tests equally weighted at 23.75% will constitute the final grade.
Test Dates:
  Wednesday February 5, 2015
  Wednesday March 5, 2015
  Wednesday April 2, 2015
  Tuesday April 29, 2015 (regular exam period 8:00 am - 10:30 am)
The exams will have two parts:
  In-class portion taken during the regular class or exam period. The in-class portion will be closed-book designed to test basic concepts and will be weighted at 80% of the test grade.
  Take-home component. The take-home section be open book and open notes and may include computer simulations and will be weighted at 20% of the test grade.
  Assume you are to work on all assignments alone unless told otherwise.

## Slide 3: Modeling
System
Biological
Mechanical
Electrical
Chemical
Financial ?
Social ??
Inputs
Outputs
Internal
Behavior
Theory: a limited statement regarding the cause and effect in a specific situation. 1
Model: A prediction of the cause and effect behavior of the system based on a theory. Since the hypothesis may be limited, the model may not represent the true nature of the system.
Goal as an engineer: Predict (and control) the “behavior” of the system.
Extreme Example: Harold Chestnut, IFAC Control Engineering Textbook Prize, formed the “Supplemental Ways of Improving International Stability (SWIIS) Foundation" to identify and implement "supplemental ways to improve international stability".1 (i.e. how to manipulate the world for good)
1. http://en.wikipedia.org/wiki/Harold_Chestnut

## Slide 4: What is Systems Engineering?
System
System Engineering addresses:
“The need to identify and manipulate the properties of a system as a whole, which in complex engineering projects may greatly differ from the sum of the parts' properties … ”1
Internal
Behavior
1. Arthur D. Hall (1962). A Methodology for Systems Engineering. Van Nostrand Reinhold. ISBN 0442030460. via http://en.wikipedia.org/wiki/Systems_engineering
Inputs
Outputs

## Slide 5: Linear Versus Nonlinear Systems
System
Linear
Nonlinear
Linear System: Given two system inputs and their respective outputs:
then a linear system must satisfy
for any scalar values and .
Nonlinear System: Not a linear system.
Tools are well developed to understand (e.g. stability) and control the behavior of linear systems.
Tools are less well developed and less general.

## Slide 6: ECE 874 Course Overview
Book: Marquez – Nonlinear Control Systems – Analysis and Design
  Background and Mathematical Tools (Chp 1-2)
  Lyapunov Stability (Ch 3, 4)
    What can we say about the time evolution of a system’s states?
  Stabilization (Ch 5)
    Controlling a nonlinear system
  Input-Output Stability (Ch6)
    Interconnected systems
  Dissipative (Ch 8, 9)
  Feedback linearization (Ch 10, 11)
  Observer Design (Ch 11)
Additional class notes.

## Slide 8
f (damping)
fk (spring)
f(t) (input forces - gravity)
Time Invariant:
f(t) =mg and is not explicitly dependent on time
Linear differential equation
x2 = velocity
x1 = position
Linear Model:
No multiplication, square, sin(), etc of the states x1 and x2

## Slide 9
State-space form of the linear model of the mass-spring-damper system
State-space form

## Slide 10
Simulation of the response of the system to initial conditions
x2 = velocity of mass
x1 = position of mass
Time
Initial
Condition
Equilibrium
Condition
20
-10
0

## Slide 11
Plot the trajectory of the states.
x2
x1
x1
x2
1
2
3
4
1
2
3
4
Plots made using pplane8.m software an MATLAB
States individually versus time
State x2 versus State x1
A phase portrait is a plot of the trajectories of the states of a dynamical system. Each initial condition produces a curve or point.

## Slide 12
x2
x1
x1
x2
1
2
3
4
1
2
3
4
A phase portrait is a plot of the trajectories of the states of a dynamical system. Each initial condition produces a curve or point.
Special point from which trajectory doesn’t move is called a critical point.
Solve by setting the derivatives = zero.
Burg using pplane8.m
States individually versus time
State 2 versus State 1
System response to initial condition:
x1 =19.6 and x2 =0

## Slide 13
The vector field arrows help sketch the system:
*

## Slide 14
x1 | x2 | f1 | f2
0 | 0 | 0 | 9.8
19.6 | 0 | 0 | 0
10 | 0 | 0 | 4.8
30 | 0 | 0 | -5.2
20 | 10 | 10 | -.2
20 | 5 | 5 | -.2
15 | 5 | 5 | 2.3
For the mass-spring-damper example:
Plot enough points to sketch the trajectories.

## Slide 15
A phase portrait is a plot of the trajectories of the states of a dynamical system. Each initial condition produces a curve or point.
Mostly interesting for second- or third-order systems.
Burg using pplane8.m
- are the initial conditions

## Slide 16
Phase portraits of linear systems are well defined
Example
Slotine and Li, Applied Nonlinear Control, page 33,
If we change the parameters in the mass-spring-damper system, which of these plots can we have?

## Slide 17
nth order differential equation
Multi-input
Explicit dependence on time is possible
Multi-output
MIMO = Multi-Input Multi-Output
SISO = Single-Input Single-Output

## Slide 18
Not an Explicit dependence on time (doesn’t appear directly, also called “time invariant”)
Still have an Implicit dependence on time (states vary with time , also called “time varying”)

## Slide 19
Mass doesn’t move from the point where gravity and spring force balance (net force is zero) when there is no velocity (no kinetic energy).

## Slide 20
"Pendulum 190deg" by Lucas V. Barbosa (Kieff) - Own work. Licensed under Public Domain via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Pendulum_190deg.gif#mediaviewer/File:Pendulum_190deg.gif
http://en.wikipedia.org/wiki/Pendulum_(mathematics)#math_Eq._1
Pendulum
Phase Portrait
Phase Portrait
Equilibrium
Point

## Slide 21
Makes this nonlinear
Can we “solve” the nonlinear differential equation directly?
Not in general
But this model still has useful information
Most of the tools we develop will tells us about the system without actually “solving” the system.
This is an autonomous system

## Slide 22
In Matlab:
>P=[-a^2*k/m 0 –k/m g]
>roots
>0.9076, -0.45+j0.8, -0.45-j0.8,
Equilibrium point

## Slide 23
Input voltage creates current in the magnetic winding which produces a force on the ball.
Ball
Resistor
This will create a strong nonlinearity
As a control problem, you would control v(t) with a computer and measure the ball position in order to control the ball’s (vertical) position.
(from the air)
(Electromechanical System)
fk
F
mg
(Mechanical Sub-system)

## Slide 24
Geometric and material properties – constants.
L
y
2nd order system
Always F<0, pulls ball to coil
Notes: Plot of actual inductance: http://cegt201.bradley.edu/projects/proj2003/maglev/

## Slide 25
(Mechanical Sub-system)
What have we achieved?
Are we finished?
Depends on how we create current.

## Slide 26
+
-
v(t)
+
-
vR
R
L(y)
1st order system
(Electrical Sub-system)

## Slide 27
“Chained” system
Roughly:
Apply voltage (v) -> produces current (x3) -> produces force (x32) -> positions ball (x1 ,x2)
Linearized model does not work well for this system.
Ball position, ball velocity, current
Repeating:
(Mechanical Sub-system)
V(t)
X3(t)
X2(t)
X1(t)
Electrical

## Slide 28
L
Coordinates of the center of mass
Input force fx

## Slide 29
As a control problem, you would control fx with a computer and measure the pendulum position in order to balance the pendulum.
4th order differential equation
A linearized model can be used to control the system.

## Slide 31
As a control problem, you would control (t) with a computer and measure the ball position in order to control the ball’s position along the beam.

## Slide 32: Chapter 1 Conclusions
Hopefully you are convinced that there are interesting problems that are nonlinear and are motivated to learn new analysis and control techniques.

## Slide 33: Homework 1
Download and install PPlane8 software (address on website)
  2D phase portraits
Problems 1.1 (the requested plot is not a phase portrait), 1.2, 1.4
Use PPlane8 to reproduce the phase portraits (PPs) for the linear system examples 1.7-1.11
Use PPlane8 to draw PP of equations 1.25 and 1.26 with =1, what happens for other values of ? (Use axes limits -4<x1,x2<4)
Plot PP of system (use axes limits -2<x1,x2<2)
Plot PP of system (use axes limits -2<x1,x2<2)
Find the equilibrium point(s) for the state-space model in the magnetic suspension example. Assume all parameters are 1 except g and assume a constant applied voltage v.

## Slide 34
Part 1.a
Homework – Solution

## Slide 35
Part 1.b
Homework – Solution

## Slide 36
Homework – Solution

## Slide 37
Homework – Solution

## Slide 38: Homework – Solution
Example: Nonlinear System, Khalil, Nonlinear Systems, 3rd ed, page 78
Burg using pplane8.m

## Slide 39
Example: Nonlinear System, Khalil, Nonlinear Systems, 3rd ed, page 78, prob 2.4-(2)
Burg using pplane8.m
Homework – Solution

## Slide 40
For a constant voltage
Homework – Solution
X1
Notes: http://www.abcm.org.br/pt/wp-content/anais/cobem/2009/pdf/COB09-0284.pdf

## Slide 41
Homework – Solution
Equilibrium point for the state-space model in the magnetic suspension: